## Slide 1: Draft Fifth Pacific Northwest Electric Power and Conservation Plan

## Slide 2: The plan in summary
Aggressive development of conservation
Confirm and develop demand response resource
Moderate near-term commercial scale development of wind to confirm costs, availability
Be prepared to begin construction of
  Coal-fired generation by 2010;
  Significant wind shortly thereafter;
  Gas-fired generation late in planning period
Address key policy issues
  Adequacy standards Transmission BPA future role

## Slide 3: Goal of this plan…
Help assure an adequate, efficient, economical and reliable power system
By identifying a robust, flexible plan for managing power system costs and risks in the face of future uncertainty
Notes: The goal of this plan is that defined by the Act – helping the region secure an adequate, efficient, economical and reliable power supply.
To do that we know we need to identify a robust and flexible plan for managing costs and risks. The future is uncertain. What we need is a plan that performs well over a wide range of future uncertainties.

## Slide 4: Where are we now, surplus or deficit?
Currently a regional surplus BUT
  Most surplus owned by Independent Power Producers (IPPs), not regional utilities
  Many NW utilities energy short
IPP generation
  Available to region but at market price, subject to market risk
Surplus/Deficit (aMW)
Load
Forecast
Notes: The chart shows the Council’s estimates of the critical water Surplus/deficit situation for the med-hi, med, and med low load forecasts. With medium load growth the surplus lasts until 2010. What’s different about this surplus for the past is that most of the surplus generation is owned by IPPs instead of regional utilities. IPPs don’t have firn transmission access to markets outside the region.
The Council believes this generation is available to the region, but at market prices and subject to market risk.

## Slide 5: Developing the plan
Identify and characterize Resources
Identify and quantify key Uncertainties
  * Loads * Hydro conditions * Fuel prices
  *Penalties on CO2 emissions * Forced outages * Market price of electricity
Evaluate cost of operating and expanding power system for 1000+ Plans over 750 Futures
  Plans – amounts and types of resources and when to be prepared to start construction
  Futures – scenarios that combine the key uncertainties over the 20 year planning period
Seek out plans that minimize average costs for given level of Risk (expensive outcomes)
Notes: The Council goes through a rigorous analytical process in developing its plan.
First, we forecast the potential demand for electricity and identify resource options for meeting the demand. The potential resources are evaluated in terms of their costs and other pertinent characteristics
To develop a plan that is robust in the face of an uncertain future, we need to define and explore the key uncertainties. How much variation might there be? How are the uncertainties likely to be related to one another? The key uncertainties include hydro conditions, loads, fuel prices, potential penalties for CO2 emissions, forced outages of power plants, and the market price of electricity. To characterize these uncertainties we rely on both analysis and expert judgment.
We then test different a thousand or more Plans (the resource types, amounts, and earliest be prepared to begin construction dates) against a large number (750) of futures (scenarios that combine possible behaviors of the key uncertainties over the 20 year planning horizon). We calculate the cost of operating and expanding the power system for each plan within the 750 alternative futures. We utilize sophisticated search techniques to seek the plans that result in the lowest average cost (over the 750 futures) for given levels of risk. The risk measure is a indicator of the potential for very expensive outcomes.

## Slide 6: The “Supply Curve”
Notes: The primary resource alternatives are represented in this “Supply Curve”
The chart represents the cumulative amount of power available at any cost (caveat – generation is represented by typical unit sizes) The costs are expressed as “levelized costs” to permit comparison of resources with different characteristics on an “apples to apples” basis.
Two take aways:
The green points – there is a lot of conservation available at relatively low cost.
The “whiskers” represent the worst and best case combinations of factors (e.g. fuel prices, carbon emissions fees, capacity etc) affecting the costs of the different resources. There is considerable uncertainty around some of the resource choices.

## Slide 7: Conservation
2500 aMW
Over last 22
years
Looking ahead – Over 2500 aMW < .05/kWh;
Avg cost $.024/kWh
Notes: Conservation is the highest priority resource under the Act. The region has accomplished a great deal over the last 20 years. But there is more to do. Over 2200 avg mw at costs less than 4 cents/kwh; over 2500 aMw at costs less than 5 cents/kwh. No, we haven’t done all the conservation. Most of this conservation is the consequence of new technologies, growth in the region and higher avoided costs.

## Slide 8: Demand Response
Demand response-- voluntary, temporary reductions or shifts in load
  Response to price volatility, reliability issues
Not a part of past plans
But 2000-2001 proved its importance
With changes in economy, can it be developed in substantial quantity at reasonable costs?
Notes: This is the first time that the Council has included demand response as part of its plan. It’s not conservation, but it is a relatively inexpensive way of avoiding extreme high prices and maintaining reliability.
It was used quite successfully in 2000-2001. However, much of it came from the AL industry, which is no longer as significant. How much DR can be developed now and at what cost is somewhat uncertain

## Slide 9: Key uncertainties
Hydro –
  Annual generation can vary +/- 4000 avg MW about mean – system must accommodate this variation
Loads –
  Long term trends and shorter term variations, e.g. economic and weather cycles
Fuel prices, particularly natural gas
  Long term trends and shorter-term volatility; e.g.“boom-bust” cycles and weather-driven volatility
Notes: Hydro is a source of uncertainty that the region has always had to deal with.
Load uncertainty – both in respect to long-term trends and shorter term variations (e.g. economic cycles) poses a particular risk for high capital cost, long-lead time resources.
Fuel price uncertainty is a particular concern for natural gas-fired resources. There is considerable uncertainty regarding the long term trends and shorter-term volatility associated with “boom-bust” cycles of development

## Slide 10: Key Uncertainties (cont.)
Climate change mitigation policy
  Growing agreement that there will be some kind of control on CO2 emissions, but when, how much very uncertain
Market price of electricity
  It is West Coast market – not determined solely by NW actions
  Market can be volatile
  Risk of having too many resources when market prices are low; having too few resources when market is high
Notes: Climate change mitigation is a growing risk for carbon-intensive fuels. There is growing agreement that some efforts to control CO2 emissions are likely at some time, but how much, when etc very uncertain
Market price of electricity is important because we can never match loads and resources perfectly – particularly with the amount of variation in the hydro system. There was a robust market in the West before the efforts at restructuring and there will continue to be one. However, it can be a source of risk. If you have too many resources and the market is low, you have to bear fixed costs with little return (early ’80s). If the converse is true, you are forced to purchase from the market when it is high (2000-2001)

## Slide 11: The Portfolio Model
Evaluates average cost and risk of operating and expanding power system for alternative Plans over 750 Futures
Does this for 1000+ plans
Seeks out plans that minimize average cost for a given level of risk

## Slide 12
D
A
B
C
Choosing
A Plan
D
Notes: The most efficient of the plans identified – those with the minimum cost for a given level of risk – are plotted on this chart with average cost on the horizontal axis and risk on the vertical
It is instructive to look at a few of these plans.
The one with the highest risk(A) relies entirely on conservation and the market
If we want to reduce risk, it is necessary to add some resources. B shows a plan with just conservation and wind.
If you want to reduce risk further, additional resources are necessary. Since B incorporated all the available wind generation, C incorporates some coal fired generation
D -- The very least risk plan adds to gas fired generation to reduce risk to the lowest level.
There were many additional plans evaluated but all involved higher costs

## Slide 13: Common characteristics of the least cost plans
All include “aggressive” conservation
  700 aMW over next 5 years; 2500 aMW over 20 years
All include demand response
  Up to 2000 MW by 2016 – dispatches when prices > $150/MW-hr
None require start of construction of generating resources before 2010
  From regional standpoint, reliance on market and conservation thru end of decade appears less costly than developing additional generation
Moving down the efficient frontier (lowering risk)
  Increasing costs of being prepared to develop additional resources and developing if necessary – insurance premium

## Slide 14: The choice of a plan
Cost and risk measures necessary but not sufficient to choose a plan
Other factors are considered, e.g.,
  Non power system costs and non-monetary effects associated with high cost outcomes not captured in cost/risk measures
  Retail rates and rate stability
  Level of dependence on imports/Power supply adequacy
Council’s recommendation – the lowest risk, least cost-plan
Notes: Looking a average cost and the risk measure are important screening tools but it is important to look beyond them in choosing a plan.
For example, those measures don’t reflect non-power system cost or the social and economic disruption that can accompany very high cost outcomes.
We also value low rates and rate stability that these measure don’t capture.
There are also concerns about power supply adequacy and the degree of reliance on imports.
The Council has looked at all these issues and has chosen the lowest risk, least cost plan.

## Slide 15: Recommended plan
Development schedule will differ for different futures (www.nwcouncil.org/dropbox/Olivia and Portfolio Model/L24X-376-P1.zip)

## Slide 16: 700 aMW conservation over 5-years? – a challenge but doable
We’ve done that much at times in past
  Less than average annual achievement from all sources 1991-02
  Utility system has spent more in the past
  Greater experience and improved acquisition tools – codes and standards processes, Alliance,
  Many major utilities have conservation targets at or near this level
Mostly taps new sources of improved efficiency
  Nearly two-thirds is new measures or new applications
  40% is lost-opportunities that are not available yet
  Getting it all means making PNW 10% more efficient over 20 years
There is a rate impact but
  About 2/3 of cost of meeting target is already in current rates
  Additional cost ~$50 - $75 million/yr = less than 1% of regional utility revenue requirements
Notes: The Council understands that it will not be easy for the region to do this level of conservation, but it believes it is doable.
We’ve done it in the past, we’ve spent that much in the past, and we have more experience and better tools. Several major utilities have plans that reflect this level
The conservation is there to do – it mostly new sources, like improved efficiency in homes, buildings, appliances and so on that have yet to be built and new technologies. Putting it in perspective, it means making the NW 10 percent more efficient in its use of electricity over the next 20 years.
The Council recognizes that there are rate impacts and that these are a concern in a region that has been battered by rate increases in the recent past. But most of the costs are already in utility budgets now. The increase amounts to less than a 1% increase in utility revenue requirements

## Slide 17: And, doing less conservation is more costly and more risky
Base – 700 aMW 5-yrs, 2540 20-yrs
Reduced – 500 aMW 5-yrs, 2480 20-yrs
Minimium – 250 aMW 5-yrs, 1450 20-yrs
Decreasing Conservation
Increasing cost and risk
Notes: The most important point is that doing less conservation costs the region more and increases risk. The base case represents the Council’s best judgment of maximum practical implementation. The reduced case primarily cuts back on the rate implementation in the first 10 years of the planning period. For the minimum case, the rate of implementation in the early years reflects what we saw during the late 70s. The effects are quite clear. Reducing implementation in the early years increases costs and risk because the conservation is not in place to avoid higher costs later on. Reducing conservation overall increases costs and risk dramatically.
It’s a question of pay now or pay more later.

## Slide 18: The Action Plan – what needs to happen over next 5 years
Develop resources now that can reduce cost and risk to the region
  700 average megawatts of conservation, 2005 – 2009
  500 megawatts of demand response, 2005 – 2009
  Secure cost-effective lost opportunity cogeneration and renewable energy projects

## Slide 19: Alternative Conservation Scenarios

## Slide 20: Total Residential Sector Cost-Effective & Realistically Achievable

## Slide 21: Residential Compact Fluorescent Lamps
30 sockets/home potential
18 sockets/home achievable
60 Watts to 13 Watts average reduction
Target ~11 million per year 2005-2009 for 160 aMW
Levelized cost 1.7 cents/kWh
Up to 20% of near-term targets

## Slide 22: Residential Heat Pump Water Heaters
Lots of electric water heaters in place
200 MWa by 2025 @4.3 cents per kWh levelized
1 of 4 DHW replacements
Availability, cost & reliability issues
Possible regional program for economy of scale

## Slide 23: Total Commercial Sector Realistically Achievable Potential = 1105 aMW (Medium Forecast – 2025)

## Slide 24: Power Supplies in Equipment
US stock 2.5 billion units
Use 6% of US electricity
15-50% savings
155 MWa PNW in 2025
TV
Cordless phone
Computers
Visa machine
Answering machines
Chargers

## Slide 25: Packaged Refrigeration Appliances
Reach-in Refrigerators & Freezers
Ice Makers
Beverage Merchandisers
Walk-ins
Vending Machines
Water Coolers
70 MWa PNW savings

## Slide 26
Process optimization
Sensors & controls
Remote monitoring
Training
Municipal Sewage Treatment
832 PNW facilities
2000 MGD total treated flow
340 MWa total electricity use
30% to 70% documented savings in small & mid-size plants
Many non-energy benefits
60 MWa savings potential

## Slide 27: Commercial Sector Realistically Achievable Potential for Buildings = 685 aMW (Medium Forecast - 2025)

## Slide 28: Commercial Lighting
About 20 separate lighting measures
Significant improvement in fluorescent lamp & ballast technology
Improvements in metal halide lighting
Improvements in incandescent spot lighting
More efficient lighting designs & fixtures
Daylighting in warehouses, schools, some retail
Needs training, product availability

## Slide 29: Industrial Sector Conservation Potential
Estimate of 5% of 2025 forecast loads
350 aMW at 1.8 cents per kWh
  Process controls
  Drive systems
  Lighting
  Refrigeration
Significant uncertainty around estimate
  Changes in region’s industrial mix

## Slide 30: Key windpower assumptions - I
Capital cost: Capital costs (overnight, yr 2000) range from $930/kW (large project) to $1120/kW (small project). $1010/kW on average. E.g., all-in of $1070/kW (2004$) for IPP-financed project in 2004. Moderately certain.
Technology Improvement: 10% cost reduction with each doubling of forecast global capacity (2%/yr average cost reduction 2005–24). Uncertain, but consistent w/last 10–15 yrs.

## Slide 31: Key windpower assumptions - II
Shaping: $4/MWh for first 2500 MW of new capacity, $8/MWh thereafter. Based on PacifiCorp & Bonneville work. Increasing shaping load on existing system may be offset by geographic diversity. Highly uncertain.
Developable new capacity: West of Continental Divide: 2500 MW high quality (30% CF); 2500 MW moderate quality (28% CF). Central MT: Very large high quality resource (36% CF), transmission-limited to local development. Professional judgement of industry reps; Uncertain.

## Slide 32: Key windpower assumptions - III
PTC: $8.95/MWh mean levelized in 2005, declining to $1.50/MWh in 2025. Very uncertain.
Green tags: $6/MWh mean levelized in 2004, declining to $1.50/MWh in 2025. Very uncertain, probably high.
Other:
  Fixed O&M - $20/kW/yr
  Variable O&M - $1.00/MWh (land rent)
  Transmission - $15/kW/yr + 1.9% loss assessment

## Slide 33: Opportunities for public comment
Public Hearings:
  Tuesday, Oct. 12, Missoula
  Tuesday, Oct. 26, Portland.
  Wednesday, Oct. 27, Eugene
  Thursday, Oct. 28, Tri Cities
  Monday, Nov. 1, Twin Falls
  Monday, Nov. 8, Boise
  Wednesday, Nov. 10, Seattle
  Tuesday, Nov. 16, CdA Id
  Wed, Nov 17, Spokane
Comments close Nov 19
Send comments to
Mark Walker Director of Public Affairs Northwest Power & Conservation Council 851 SW 6th Avenue, Suite 1100 Portland, Oregon 97204-1348 fax 503-820-2370 or email comments@nwcouncil.org

## Slide 34
http://www.nwcouncil.org/energy/powerplan/
draftplan/Default.htm