## Slide 1
© 2007 Pearson Prentice Hall
This work is protected by United States copyright laws and is provided solely for the use of instructors in teaching their courses and assessing student learning. Dissemination or sale of any part of this work (including on the World Wide Web) will destroy the integrity of the work and is not permitted. The work and materials from it should never be made available to students except by instructors using the accompanying text in their classes. All recipients of this work are expected to abide by these restrictions and to honor the intended pedagogical purposes and the needs of other instructors who rely on these materials.
ConcepTest PowerPoints
Chapter 20
College Physics
6th Edition
Wilson / Buffa / Lou

## Slide 2: ConcepTest 20.1a Magnetic Flux I
<footer>
<date/time>
In order to change the magnetic flux through the loop, what would you have to do?
1) drop the magnet
2) move the magnet upward
3) move the magnet sideways
4) only (1) and (2)
5) all of the above

## Slide 3: ConcepTest 20.1a Magnetic Flux I
<footer>
<date/time>
Moving the magnet in any direction would change the magnetic field through the loop and thus the magnetic flux.
In order to change the magnetic flux through the loop, what would you have to do?
1) drop the magnet
2) move the magnet upward
3) move the magnet sideways
4) only (1) and (2)
5) all of the above

## Slide 4: ConcepTest 20.1b Magnetic Flux II
<footer>
<date/time>
1) tilt the loop
2) change the loop area
3) use thicker wires
4) only (1) and (2)
5) all of the above
In order to change the magnetic flux through the loop, what would you have to do?

## Slide 5: ConcepTest 20.1b Magnetic Flux II
<footer>
<date/time>
1) tilt the loop
2) change the loop area
3) use thicker wires
4) only (1) and (2)
5) all of the above
Since  = B A cos , changing the area or tilting the loop (which varies the projected area) would change the magnetic flux through the loop.
In order to change the magnetic flux through the loop, what would you have to do?

## Slide 6: ConcepTest 20.2a Moving Bar Magnet I
<footer>
<date/time>
If a south pole moves toward the loop from behind the page, in what direction is the induced current?
1) clockwise
2) counterclockwise
3) no induced current

## Slide 7: ConcepTest 20.2a Moving Bar Magnet I
<footer>
<date/time>
If a south pole moves toward the loop from behind the page, in what direction is the induced current?
1) clockwise
2) counterclockwise
3) no induced current
The magnetic field of the moving bar magnet is pointing into the page and getting larger as the magnet moves closer to the loop. Thus the induced magnetic field has to point out of the page. A counterclockwise induced current will give just such an induced magnetic field.
Follow-up: What happens if the magnet is stationary but the loop moves?

## Slide 8: ConcepTest 20.2b Moving Bar Magnet II
<footer>
<date/time>
If a north pole moves toward the loop in the plane of the page, in what direction is the induced current?
1) clockwise
2) counterclockwise
3) no induced current

## Slide 9: ConcepTest 20.2b Moving Bar Magnet II
<footer>
<date/time>
Since the magnet is moving parallel to the loop, there is no magnetic flux through the loop. Thus the induced current is zero.
If a north pole moves toward the loop in the plane of the page, in what direction is the induced current?
1) clockwise
2) counterclockwise
3) no induced current

## Slide 10: ConcepTest 20.3a Moving Wire Loop I
<footer>
<date/time>
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
A wire loop is being pulled through a uniform magnetic field. What is the direction of the induced current?
1) clockwise
2) counterclockwise
3) no induced current

## Slide 11: ConcepTest 20.3a Moving Wire Loop I
<footer>
<date/time>
Since the magnetic field is uniform, the magnetic flux through the loop is not changing. Thus no current is induced.
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
A wire loop is being pulled through a uniform magnetic field. What is the direction of the induced current?
1) clockwise
2) counterclockwise
3) no induced current
Follow-up: What happens if the loop moves out of the page?

## Slide 12: ConcepTest 20.3b Moving Wire Loop II
<footer>
<date/time>
1) clockwise
2) counterclockwise
3) no induced current
A wire loop is being pulled through a uniform magnetic field that suddenly ends. What is the direction of the induced current?
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x

## Slide 13: ConcepTest 20.3b Moving Wire Loop II
<footer>
<date/time>
1) clockwise
2) counterclockwise
3) no induced current
A wire loop is being pulled through a uniform magnetic field that suddenly ends. What is the direction of the induced current?
The B field into the page is disappearing in the loop, so it must be compensated by an induced flux also into the page. This can be accomplished by an induced current in the clockwise direction in the wire loop.
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
Follow-up: What happens when the loop is completely out of the field?

## Slide 14: ConcepTest 20.3c Moving Wire Loop III
<footer>
<date/time>
1) clockwise
2) counterclockwise
3) no induced current
What is the direction of the induced current if the B field suddenly increases while the loop is in the region?
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x

## Slide 15: ConcepTest 20.3c Moving Wire Loop III
<footer>
<date/time>
1) clockwise
2) counterclockwise
3) no induced current
What is the direction of the induced current if the B field suddenly increases while the loop is in the region?
The increasing B field into the page must be countered by an induced flux out of the page. This can be accomplished by induced current in the counterclockwise direction in the wire loop.
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x x x x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
x x x x x
Follow-up: What if the loop stops moving while the field increases?

## Slide 16: ConcepTest 20.4 Shrinking Wire Loop
<footer>
<date/time>
1) clockwise
2) counterclockwise
3) no induced current
If a coil is shrinking in a magnetic field pointing into the page, in what direction is the induced current?

## Slide 17: ConcepTest 20.4 Shrinking Wire Loop
<footer>
<date/time>
The magnetic flux through the loop is decreasing, so the induced B field must try to reinforce it and therefore points in the same direction—into the page. According to the right-hand rule, an induced clockwise current will generate a magnetic field into the page.
1) clockwise
2) counterclockwise
3) no induced current
If a coil is shrinking in a magnetic field pointing into the page, in what direction is the induced current?
Follow-up: What if the B field is oriented at 90° to its present direction?

## Slide 18: ConcepTest 20.6a Voltage and Current I
<footer>
<date/time>
N
S
N
S
1
2
1) V1 > V2
2) V1 < V2
3) V1 = V2  0
4) V1 = V2 = 0
Wire 1 (length L) forms a one-turn loop, and a bar magnet is dropped through. Wire 2 (length 2L) forms a two-turn loop, and the same magnet is dropped through. Compare the magnitude of the induced voltages in these two cases.

## Slide 19: ConcepTest 20.6a Voltage and Current I
<footer>
<date/time>
Faraday’s Law:
depends on N (number of loops) so the induced emf is twice as large in the wire with 2 loops.
N
S
N
S
1
2
1) V1 > V2
2) V1 < V2
3) V1 = V2  0
4) V1 = V2 = 0
Wire 1 (length L) forms a one-turn loop, and a bar magnet is dropped through. Wire 2 (length 2L) forms a two-turn loop, and the same magnet is dropped through. Compare the magnitude of the induced voltages in these two cases.

## Slide 20: ConcepTest 20.6b Voltage and Current II
<footer>
<date/time>
N
S
N
S
1
2
1) I1 > I2
2) I1 < I2
3) I1 = I2  0
4) I1 = I2 = 0
Wire 1 (length L) forms a one-turn loop, and a bar magnet is dropped through. Wire 2 (length 2L) forms a two-turn loop, and the same magnet is dropped through. Compare the magnitude of the induced currents in these two cases.

## Slide 21: ConcepTest 20.6b Voltage and Current II
<footer>
<date/time>
Faraday’s law:
says that the induced emf is twice as large in the wire with 2 loops. The current is given by Ohm’s law: I = V/R. Since Wire 2 is twice as long as Wire 1, it has twice the resistance, so the current in both wires is the same.
N
S
N
S
1
2
1) I1 > I2
2) I1 < I2
3) I1 = I2  0
4) I1 = I2 = 0
Wire 1 (length L) forms a one-turn loop, and a bar magnet is dropped through. Wire 2 (length 2L) forms a two-turn loop, and the same magnet is dropped through. Compare the magnitude of the induced currents in these two cases.

## Slide 22: ConcepTest 20.7a Falling Magnet I
<footer>
<date/time>
A bar magnet is held above the floor and dropped. In 1, there is nothing between the magnet and the floor. In 2, the magnet falls through a copper loop. How will the magnet in case 2 fall in comparison to case 1?
copper
loop
N
S
2
N
S
1
1) it will fall slower
2) it will fall faster
3) it will fall the same

## Slide 23: ConcepTest 20.7a Falling Magnet I
<footer>
<date/time>
When the magnet is falling from above the loop in 2, the induced current will produce a north pole on top of the loop, which repels the magnet.
When the magnet is below the loop, the induced current will produce a north pole on the bottom of the loop, which attracts the south pole of the magnet.
A bar magnet is held above the floor and dropped. In 1, there is nothing between the magnet and the floor. In 2, the magnet falls through a copper loop. How will the magnet in case 2 fall in comparison to case 1?
copper
loop
N
S
2
N
S
1
1) it will fall slower
2) it will fall faster
3) it will fall the same
Follow-up: What happens in case 2 if you flip the magnet so that the south pole is on the bottom as the magnet falls?

## Slide 24: ConcepTest 20.7b Falling Magnet II
<footer>
<date/time>
1) induced current doesn’t need any energy
2) energy conservation is violated in this case
3) there is less KE in case 2
4) there is more gravitational PE in case 2
If there is induced current, doesn’t that cost energy? Where would that energy come from in case 2?
N
S
2
copper
loop
N
S
1

## Slide 25: ConcepTest 20.7b Falling Magnet II
<footer>
<date/time>
1) induced current doesn’t need any energy
2) energy conservation is violated in this case
3) there is less KE in case 2
4) there is more gravitational PE in case 2
If there is induced current, doesn’t that cost energy? Where would that energy come from in case 2?
In both cases, the magnet starts with the same initial gravitational PE.
In case 1, all the gravitational PE has been converted into kinetic energy.
In case 2, we know the magnet falls slower, thus there is less KE. The difference in energy goes into making the induced current.
N
S
2
copper
loop
N
S
1

## Slide 26: ConcepTest 20.8a Loop and Wire I
<footer>
<date/time>
A wire loop is being pulled away from a current-carrying wire. What is the direction of the induced current in the loop?
I
1) clockwise
2) counterclockwise
3) no induced current
Notes: [CORRECT 5 ANSWER]

## Slide 27: ConcepTest 20.8a Loop and Wire I
<footer>
<date/time>
The magnetic flux is into the page on the right side of the wire and decreasing due to the fact that the loop is being pulled away. By Lenz’s Law, the induced B field will oppose this decrease. Thus, the new B field points into the page, which requires an induced clockwise current to produce such a B field.
I
1) clockwise
2) counterclockwise
3) no induced current
A wire loop is being pulled away from a current-carrying wire. What is the direction of the induced current in the loop?

## Slide 28: ConcepTest 20.8b Loop and Wire II
<footer>
<date/time>
What is the induced current if the wire loop moves in the direction of the yellow arrow ?
1) clockwise
2) counterclockwise
3) no induced current
I
Notes: [CORRECT 5 ANSWER]

## Slide 29: ConcepTest 20.8b Loop and Wire II
<footer>
<date/time>
The magnetic flux through the loop is not changing as it moves parallel to the wire. Therefore, there is no induced current.
I
1) clockwise
2) counterclockwise
3) no induced current
What is the induced current if the wire loop moves in the direction of the yellow arrow ?

## Slide 30: ConcepTest 20.9 Motional EMF
<footer>
<date/time>
  A conducting rod slides on a conducting track in a constant B field directed into the page. What is the direction of the induced current?
x x x x x x x x x x x
x x x x x x x x x x x
x x x x x x x x x x x
x x x x x x x x x x x
v
1) clockwise
2) counterclockwise
3) no induced current

## Slide 31: ConcepTest 20.9 Motional EMF
<footer>
<date/time>
  A conducting rod slides on a conducting track in a constant B field directed into the page. What is the direction of the induced current?
x x x x x x x x x x x
x x x x x x x x x x x
x x x x x x x x x x x
x x x x x x x x x x x
v
The B field points into the page. The flux is increasing since the area is increasing. The induced B field opposes this change and therefore points out of the page. Thus, the induced current runs counterclockwise, according to the right-hand rule.
1) clockwise
2) counterclockwise
3) no induced current
Follow-up: What direction is the magnetic force on the rod as it moves?

## Slide 32: ConcepTest 20.10 Generators
<footer>
<date/time>
A generator has a coil of wire rotating in a magnetic field. If the rotation rate increases, how is the maximum output voltage of the generator affected?
1) increases
2) decreases
3) stays the same
4) varies sinusoidally

## Slide 33: ConcepTest 20.10 Generators
<footer>
<date/time>
The maximum voltage is the leading term that multiplies sin(t) and is given by  = NBA. Therefore, if  increases, then  must increase as well.
A generator has a coil of wire rotating in a magnetic field. If the rotation rate increases, how is the maximum output voltage of the generator affected?
1) increases
2) decreases
3) stays the same
4) varies sinusoidally

## Slide 34: ConcepTest 20.11 Magic Loop
<footer>
<date/time>
A wire loop is in a uniform magnetic field. Current flows in the wire loop, as shown. What does the loop do?
1) moves to the right
2) moves up
3) remains motionless
4) rotates
5) moves out of the page

## Slide 35: ConcepTest 20.11 Magic Loop
<footer>
<date/time>
There is no magnetic force on the top and bottom legs, since they are parallel to the B field. However, the magnetic force on the right side is into the page, and the magnetic force on the left side is out of the page. Therefore, the entire loop will tend to rotate.
A wire loop is in a uniform magnetic field. Current flows in the wire loop, as shown. What does the loop do?
1) moves to the right
2) moves up
3) remains motionless
4) rotates
5) moves out of the page
This is how a motor works !!

## Slide 36: ConcepTest 20.12a Transformers I
120 V
What is the voltage across the lightbulb?
1) 30 V
2) 60 V
3) 120 V
4) 240 V
5) 480 V

## Slide 37: ConcepTest 20.12a Transformers I
The first transformer has a 2:1 ratio of turns, so the voltage doubles. But the second transformer has a 1:2 ratio, so the voltage is halved again. Therefore, the end result is the same as the original voltage.
120 V
240 V
120 V
What is the voltage across the lightbulb?
1) 30 V
2) 60 V
3) 120 V
4) 240 V
5) 480 V

## Slide 38: ConcepTest 20.12b Transformers II
1) 1/4 A
2) 1/2 A
3) 1 A
4) 2 A
5) 5 A
Given that the intermediate current is 1 A, what is the current through the lightbulb?
1 A
120 V
240 V
120 V

## Slide 39: ConcepTest 20.12b Transformers II
Power in = Power out
240 V  1 A = 120 V  ???
The unknown current is 2 A.
1) 1/4 A
2) 1/2 A
3) 1 A
4) 2 A
5) 5 A
Given that the intermediate current is 1 A, what is the current through the lightbulb?
1 A
120 V
240 V
120 V

## Slide 40: ConcepTest 20.12c Transformers III
1) greater than 6 V
2) 6 V
3) less than 6 V
4) zero
A 6 V battery is connected to one side of a transformer. Compared to the voltage drop across coil A, the voltage across coil B is:
A
B
6 V

## Slide 41: ConcepTest 20.12c Transformers III
The voltage across B is zero. Only a changing magnetic flux induces an EMF. Batteries can only provide DC current.
1) greater than 6 V
2) 6 V
3) less than 6 V
4) zero
A
B
6 V
A 6 V battery is connected to one side of a transformer. Compared to the voltage drop across coil A, the voltage across coil B is:

## Slide 42: ConcepTest 20.13a EM Waves I
plastic
copper
A loop with an AC current produces a changing magnetic field. Two loops have the same area, but one is made of plastic and the other copper. In which of the loops is the induced voltage greater?
1) the plastic loop
2) the copper loop
3) voltage is same in both

## Slide 43: ConcepTest 20.13a EM Waves I
Faraday’s Law says nothing about the material:
The change in flux is the same (and N is the same), so the induced emf is the same.
plastic
copper
A loop with an AC current produces a changing magnetic field. Two loops have the same area, but one is made of plastic and the other copper. In which of the loops is the induced voltage greater?
1) the plastic loop
2) the copper loop
3) voltage is same in both

## Slide 44: ConcepTest 20.13b EM Waves II
In which of the loops is the induced current greater?
1) the plastic loop
2) the copper loop
3) current is same in both
plastic
copper

## Slide 45: ConcepTest 20.13b EM Waves II
In which of the loops is the induced current greater?
Remember that I = V / R (Ohm’s Law), and copper has smaller resistance, so the copper loop has the greater current.
1) the plastic loop
2) the copper loop
3) current is same in both
plastic
copper

## Slide 46: ConcepTest 20.13c EM Waves III
A loop with an AC current produces a changing magnetic field. Consider a copper loop, and next to it imagine a loop of air of equal size. In which of the loops will the induced electric field be greater?
air
copper
1) the plastic loop
2) the copper loop
3) electric field is same in both

## Slide 47: ConcepTest 20.13c EM Waves III
A loop with an AC current produces a changing magnetic field. Consider a copper loop, and next to it imagine a loop of air of equal size. In which of the loops will the induced electric field be greater?
air
copper
Just as in the example with the plastic loop, the induced electric field will be the same in both !
1) the plastic loop
2) the copper loop
3) electric field is same in both

## Slide 48: ConcepTest 20.14 Oscillations
The electric field in an EM wave traveling northeast oscillates up and down. In what plane does the magnetic field oscillate?
1) in the north-south plane
2) in the up-down plane
3) in the NE-SW plane
4) in the NW-SE plane
5) in the east-west plane

## Slide 49: ConcepTest 20.14 Oscillations
The magnetic field oscillates perpendicular to BOTH the electric field and the direction of the wave. Therefore the magnetic field must oscillate in the NW-SE plane.
The electric field in an EM wave traveling northeast oscillates up and down. In what plane does the magnetic field oscillate?
1) in the north-south plane
2) in the up-down plane
3) in the NE-SW plane
4) in the NW-SE plane
5) in the east-west plane

## Slide 50: ConcepTest 20.15 TV Antennas
Before the days of cable, televisions often had two antennae on them, one straight and one circular. Which antenna picked up the magnetic oscillations?
1) the circular one
2) the straight one
3) both equally; they were straight and circular for different reasons

## Slide 51: ConcepTest 20.15 TV Antennas
The varying B field in the loop means the flux is changing and therefore an EMF is induced.
Before the days of cable, televisions often had two antennae on them, one straight and one circular. Which antenna picked up the magnetic oscillations?
1) the circular one
2) the straight one
3) both equally; they were straight and circular for different reasons

## Slide 52: ConcepTest 20.16 Radio Antennas
If a radio transmitter has a vertical antenna, should a receiver’s antenna be vertical or horizontal to obtain the best reception?
1) vertical
2) horizontal
3) doesn’t matter

## Slide 53: ConcepTest 20.16 Radio Antennas
If a wave is sent out from a vertical antenna, the electric field oscillates up and down. Thus, the receiver’s antenna should also be vertical so that the arriving electric field can set the charges in motion.
E field
of wave
E field
of wave
If a radio transmitter has a vertical antenna, should a receiver’s antenna be vertical or horizontal to obtain the best reception?
1) vertical
2) horizontal
3) doesn’t matter

## Slide 54: ConcepTest 20.17 Heat Insulation
Imagine you are an alien from another planet with infrared eyes. What do you see when you look around the room?
1) bright spots where the bodies are and dark elsewhere
2) dark spots where the bodies are and bright elsewhere
3) the same as what we see, only everything looks red
4) the same as what we see, except that red is invisible

## Slide 55: ConcepTest 20.17 Heat Insulation
Bodies are sources of heat and therefore emit infrared radiation. An alien with an instrument to detect infrared would see these sources as bright spots.
Imagine you are an alien from another planet with infrared eyes. What do you see when you look around the room?
Infrared photo of a building to check the heat insulation–where are the problem spots in this case?
1) bright spots where the bodies are and dark elsewhere
2) dark spots where the bodies are and bright elsewhere
3) the same as what we see, only everything looks red
4) the same as what we see, except that red is invisible

## Slide 56: ConcepTest 20.18 Superman
1) yes, no problem
2) nope, he can’t
3) need more information
Since Superman is from the planet Krypton, his eyes are sensitive to the entire electromagnetic spectrum. Does that mean he can use x-ray vision to see that Lois Lane is being kidnapped in the other room?

## Slide 57: ConcepTest 20.18 Superman
X-ray vision means that Superman’s eyes can receive x-rays, but not send them! So what would have to happen for him to see Lois Lane being kidnapped?
1) yes, no problem
2) nope, he can’t
3) need more information
Since Superman is from the planet Krypton, his eyes are sensitive to the entire electromagnetic spectrum. Does that mean he can use x-ray vision to see that Lois Lane is being kidnapped in the other room?