## Slide 1: ConcepTest 18.1a Series Resistors I
<footer>
<date/time>
9 V
Assume that the voltage of the battery is 9 V and that the three resistors are identical. What is the potential difference across each resistor?
1) 12 V
2) zero
3) 3 V
4) 4 V
5) you need to know the actual value of R

## Slide 2: ConcepTest 18.1a Series Resistors I
<footer>
<date/time>
Since the resistors are all equal, the voltage will drop evenly across the 3 resistors, with 1/3 of 9 V across each one. So we get a 3 V drop across each.
9 V
Assume that the voltage of the battery is 9 V and that the three resistors are identical. What is the potential difference across each resistor?
1) 12 V
2) zero
3) 3 V
4) 4 V
5) you need to know the actual value of R
Follow-up: What would be the potential difference if R= 1 

## Slide 3: ConcepTest 18.1b Series Resistors II
<footer>
<date/time>
12 V
R1= 4 
R2= 2 
In the circuit below, what is the voltage across R1?
1) 12 V
2) zero
3) 6 V
4) 8 V
5) 4 V

## Slide 4: ConcepTest 18.1b Series Resistors II
<footer>
<date/time>
12 V
R1= 4 
R2= 2 
In the circuit below, what is the voltage across R1?
1) 12 V
2) zero
3) 6 V
4) 8 V
5) 4 V
The voltage drop across R1 has to be twice as big as the drop across R2. This means that V1 = 8 V and V2 = 4 V. Or else you could find the current I = V/R = (12 V)/(6  = 2 A, then use Ohm’s Law to get voltages.
Follow-up: What happens if the voltage is doubled?

## Slide 5: ConcepTest 18.2a Parallel Resistors I
<footer>
<date/time>
In the circuit below, what is the current through R1?
10 V
R1= 5 
R2= 2 
1) 10 A
2) zero
3) 5 A
4) 2 A
5) 7 A

## Slide 6: ConcepTest 18.2a Parallel Resistors I
<footer>
<date/time>
The voltage is the same (10 V) across each resistor because they are in parallel. Thus, we can use Ohm’s Law, V1 = I1 R1 to find the current I1 = 2 A.
In the circuit below, what is the current through R1?
10 V
R1= 5 
R2= 2 
1) 10 A
2) zero
3) 5 A
4) 2 A
5) 7 A
Follow-up: What is the total current through the battery?

## Slide 7: ConcepTest 18.2b Parallel Resistors II
<footer>
<date/time>
1) increases
2) remains the same
3) decreases
4) drops to zero
Points P and Q are connected to a battery of fixed voltage. As more resistors R are added to the parallel circuit, what happens to the total current in the circuit?

## Slide 8: ConcepTest 18.2b Parallel Resistors II
<footer>
<date/time>
1) increases
2) remains the same
3) decreases
4) drops to zero
As we add parallel resistors, the overall resistance of the circuit drops. Since V = IR, and V is held constant by the battery, when resistance decreases, the current must increase.
Points P and Q are connected to a battery of fixed voltage. As more resistors R are added to the parallel circuit, what happens to the total current in the circuit?
Follow-up: What happens to the current through each resistor?

## Slide 9: ConcepTest 18.3a Short Circuit I
<footer>
<date/time>
Current flows through a lightbulb. If a wire is now connected across the bulb, what happens?
1) all the current continues to flow through the bulb
2) half the current flows through the wire, the other half continues through the bulb
3) all the current flows through the wire
4) none of the above

## Slide 10: ConcepTest 18.3a Short Circuit I
<footer>
<date/time>
The current divides based on the ratio of the resistances. If one of the resistances is zero, then ALL of the current will flow through that path.
Current flows through a lightbulb. If a wire is now connected across the bulb, what happens?
1) all the current continues to flow through the bulb
2) half the current flows through the wire, the other half continues through the bulb
3) all the current flows through the wire
4) none of the above
Follow-up: Doesn’t the wire have SOME resistance?

## Slide 11: ConcepTest 18.3b Short Circuit II
<footer>
<date/time>
Two lightbulbs A and B are connected in series to a constant voltage source. When a wire is connected across B, bulb A will:
1) glow brighter than before
2) glow just the same as before
3) glow dimmer than before
4) go out completely
5) explode

## Slide 12: ConcepTest 18.3b Short Circuit II
<footer>
<date/time>
Since bulb B is bypassed by the wire, the total resistance of the circuit decreases. This means that the current through bulb A increases.
Two lightbulbs A and B are connected in series to a constant voltage source. When a wire is connected across B, bulb A will:
1) glow brighter than before
2) glow just the same as before
3) glow dimmer than before
4) go out completely
5) explode
Follow-up: What happens to bulb B?

## Slide 13: ConcepTest 18.4a Circuits I
<footer>
<date/time>
1) circuit 1
2) circuit 2
3) both the same
4) it depends on R
The lightbulbs in the circuit below are identical with the same resistance R. Which circuit produces more light? (brightness  power)

## Slide 14: ConcepTest 18.4a Circuits I
<footer>
<date/time>
1) circuit 1
2) circuit 2
3) both the same
4) it depends on R
The lightbulbs in the circuit below are identical with the same resistance R. Which circuit produces more light? (brightness  power)
In #1, the bulbs are in parallel, lowering the total resistance of the circuit. Thus, circuit #1 will draw a higher current, which leads to more light, because P = I V.

## Slide 15: ConcepTest 18.4b Circuits II
<footer>
<date/time>
1) twice as much
2) the same
3) 1/2 as much
4) 1/4 as much
5) 4 times as much
10 V
A
B
C
The three lightbulbs in the circuit all have the same resistance of 1  By how much is the brightness of bulb B greater or smaller than the brightness of bulb A? (brightness  power)

## Slide 16: ConcepTest 18.4b Circuits II
<footer>
<date/time>
1) twice as much
2) the same
3) 1/2 as much
4) 1/4 as much
5) 4 times as much
10 V
A
B
C
We can use P = V2/R to compare the power:
PA = (VA)2/RA = (10 V) 2/1  = 100 W
PB = (VB)2/RB = (5 V) 2/1  = 25 W
The three lightbulbs in the circuit all have the same resistance of 1  By how much is the brightness of bulb B greater or smaller than the brightness of bulb A? (brightness  power)
Follow-up: What is the total current in the circuit?

## Slide 17: ConcepTest 18.5a More Circuits I
<footer>
<date/time>
1) increase
2) decrease
3) stay the same
What happens to the voltage across the resistor R1 when the switch is closed? The voltage will:
V
R1
R3
R2
S

## Slide 18: ConcepTest 18.5a More Circuits I
<footer>
<date/time>
1) increase
2) decrease
3) stay the same
What happens to the voltage across the resistor R1 when the switch is closed? The voltage will:
With the switch closed, the addition of R2 to R3 decreases the equivalent resistance, so the current from the battery increases. This will cause an increase in the voltage across R1 .
V
R1
R3
R2
S
Follow-up: What happens to the current through R3?

## Slide 19: ConcepTest 18.5b More Circuits II
<footer>
<date/time>
1) increases
2) decreases
3) stays the same
V
R1
R3
R4
R2
S
What happens to the voltage across the resistor R4 when the switch is closed?
Notes: [CORRECT 5 ANSWER]

## Slide 20
<footer>
<date/time>
V
R1
R3
R4
R2
S
A
B
C
We just saw that closing the switch causes an increase in the voltage across R1 (which is VAB). The voltage of the battery is constant, so if VAB increases, then VBC must decrease!
What happens to the voltage across the resistor R4 when the switch is closed?
1) increases
2) decreases
3) stays the same
ConcepTest 18.5b More Circuits II
Follow-up: What happens to the current through R4?

## Slide 21: ConcepTest 18.6 Even More Circuits
<footer>
<date/time>
Which resistor has the greatest current going through it? Assume that all the resistors are equal.
V
R1
R2
R3
R5
R4
1) R1
2) both R1 and R2 equally
3) R3 and R4
4) R5
5) all the same

## Slide 22: ConcepTest 18.6 Even More Circuits
<footer>
<date/time>
The same current must flow through left and right combinations of resistors. On the LEFT, the current splits equally, so I1 = I2. On the RIGHT, more current will go through R5 than R3 + R4 since the branch containing R5 has less resistance.
1) R1
2) both R1 and R2 equally
3) R3 and R4
4) R5
5) all the same
Which resistor has the greatest current going through it? Assume that all the resistors are equal.
V
R1
R2
R3
R5
R4
Follow-up: Which one has the smallest voltage drop?

## Slide 23: ConcepTest 18.7 Junction Rule
1) 2 A
2) 3 A
3) 5 A
4) 6 A
5) 10 A
5 A
8 A
2 A
P
What is the current in branch P?
Notes: [CORRECT 5 ANSWER]

## Slide 24
The current entering the junction in red is 8 A, so the current leaving must also be 8 A. One exiting branch has 2 A, so the other branch (at P) must have 6 A.
5 A
8 A
2 A
P
junction
6 A
S
1) 2 A
2) 3 A
3) 5 A
4) 6 A
5) 10 A
What is the current in branch P?
ConcepTest 18.7 Junction Rule

## Slide 25: ConcepTest 18.7 Kirchhoff’s Rules
The lightbulbs in the circuit are identical. When the switch is closed, what happens?
1) both bulbs go out
2) intensity of both bulbs increases
3) intensity of both bulbs decreases
4) A gets brighter and B gets dimmer
5) nothing changes
Notes: [CORRECT 5 ANSWER]

## Slide 26
When the switch is open, the point between the bulbs is at 12 V. But so is the point between the batteries. If there is no potential difference, then no current will flow once the switch is closed!! Thus, nothing changes.
The lightbulbs in the circuit are identical. When the switch is closed, what happens?
1) both bulbs go out
2) intensity of both bulbs increases
3) intensity of both bulbs decreases
4) A gets brighter and B gets dimmer
5) nothing changes
ConcepTest 18.8 Kirchhoff’s Rules
24 V
Follow-up: What happens if the bottom battery is replaced by a 24-V battery?

## Slide 27: ConcepTest 18.9 Wheatstone Bridge
1) I
2) I/2
3) I/3
4) I/4
5) zero
An ammeter A is connected between points a and b in the circuit below, in which the four resistors are identical. The current through the ammeter is:
I
V
a
b

## Slide 28: ConcepTest 18.9 Wheatstone Bridge
Since all resistors are identical, the voltage drops are the same across the upper branch and the lower branch. Thus, the potentials at points a and b are also the same. Therefore, no current flows.
1) I
2) I/2
3) I/3
4) I/4
5) zero
An ammeter A is connected between points a and b in the circuit below, in which the four resistors are identical. The current through the ammeter is:
I
V
a
b

## Slide 29: ConcepTest 18.10 More Kirchhoff’s Rules
2 V
2 
2 V
6 V
4 V
3 
1 
1 
I1
I3
I2
Which of the equations is valid for the circuit below?
1) 2 – I1 – 2I2 = 0
2) 2 – 2I1 – 2I2 – 4I3 = 0
3) 2 – I1 – 4 – 2I2 = 0
4) I3 – 4 – 2I2 + 6 = 0
5) 2 – I1 – 3I3 – 6 = 0

## Slide 30: ConcepTest 18.10 More Kirchhoff’s Rules
2 V
2 
2 V
6 V
4 V
3 
1 
1 
I1
I3
I2
Equation 3 is valid for the left loop: The left battery gives +2V, then there is a drop through a 1 resistor with current I1 flowing. Then we go through the middle battery (but from + to – !), which gives –4V. Finally, there is a drop through a 2 resistor with current I2.
Which of the equations is valid for the circuit below?
1) 2 – I1 – 2I2 = 0
2) 2 – 2I1 – 2I2 – 4I3 = 0
3) 2 – I1 – 4 – 2I2 = 0
4) I3 – 4 – 2I2 + 6 = 0
5) 2 – I1 – 3I3 – 6 = 0