## Slide 1: ConcepTest 17.3a Wires I
<footer>
<date/time>
Two wires, A and B, are made of the same metal and have equal length, but the resistance of wire A is four times the resistance of wire B. How do their diameters compare?
1) dA = 4 dB
2) dA = 2 dB
3) dA = dB
4) dA = 1/2 dB
5) dA = 1/4 dB

## Slide 2: ConcepTest 17.3a Wires I
<footer>
<date/time>
The resistance of wire A is greater because its area is less than wire B. Since area is related to radius (or diameter) squared, the diameter of A must be two times less than B.
Two wires, A and B, are made of the same metal and have equal length, but the resistance of wire A is four times the resistance of wire B. How do their diameters compare?
1) dA = 4 dB
2) dA = 2 dB
3) dA = dB
4) dA = 1/2 dB
5) dA = 1/4 dB

## Slide 3: ConcepTest 17.3b Wires II
<footer>
<date/time>
A wire of resistance R is stretched uniformly (keeping its volume constant) until it is twice its original length. What happens to the resistance?
1) it decreases by a factor 4
2) it decreases by a factor 2
3) it stays the same
4) it increases by a factor 2
5) it increases by a factor 4

## Slide 4: ConcepTest 17.3b Wires II
<footer>
<date/time>
Keeping the volume (= area x length) constant means that if the length is doubled, the area is halved.
Since , this increases the resistance by four.
A wire of resistance R is stretched uniformly (keeping its volume constant) until it is twice its original length. What happens to the resistance?
1) it decreases by a factor 4
2) it decreases by a factor 2
3) it stays the same
4) it increases by a factor 2
5) it increases by a factor 4

## Slide 5: ConcepTest 17.4 Dimmer
When you rotate the knob of a light dimmer, what is being changed in the electric circuit?
1) the power
2) the current
3) the voltage
4) both (1) and (2)
5) both (2) and (3)

## Slide 6: ConcepTest 17.4 Dimmer
The voltage is provided at 120 V from the outside. The light dimmer increases the resistance and therefore decreases the current that flows through the lightbulb.
When you rotate the knob of a light dimmer, what is being changed in the electric circuit?
1) the power
2) the current
3) the voltage
4) both (1) and (2)
5) both (2) and (3)
Follow-up: Why does the voltage not change?

## Slide 7: ConcepTest 17.5a Lightbulbs
Two lightbulbs operate at 120 V, but one has a power rating of 25 W while the other has a power rating of 100 W. Which one has the greater resistance?
1) the 25 W bulb
2) the 100 W bulb
3) both have the same
4) this has nothing to do with resistance

## Slide 8: ConcepTest 17.5a Lightbulbs
Since P = V2 / R , the bulb with the lower power rating has to have the higher resistance.
Two lightbulbs operate at 120 V, but one has a power rating of 25 W while the other has a power rating of 100 W. Which one has the greater resistance?
1) the 25 W bulb
2) the 100 W bulb
3) both have the same
4) this has nothing to do with resistance
Follow-up: Which one carries the greater current?

## Slide 9: ConcepTest 17.5b Space Heaters I
Two space heaters in your living room are operated at 120 V. Heater 1 has twice the resistance of heater 2. Which one will give off more heat?
1) heater 1
2) heater 2
3) both equally

## Slide 10: ConcepTest 17.5b Space Heaters I
Using P = V2 / R, the heater with the smaller resistance will have the larger power output. Thus, heater 2 will give off more heat.
Two space heaters in your living room are operated at 120 V. Heater 1 has twice the resistance of heater 2. Which one will give off more heat?
1) heater 1
2) heater 2
3) both equally
Follow-up: Which one carries the greater current?